## Slide 1
Vehicle and Incident Detection and Classification
from Existing INDOT CCTV Feeds
Contacts: Stanley Chien, Yaobin Chen, Zhengming Ding, TASI, IUPUI, schien@iupui.edu; Jim Sturdevant, TMC, INDOT, jsturdevant@indot.in.gov
Abstract
INDOT has installed hundreds of cameras on Indiana highways to monitor the traffic conditions. Currently the camera videos are monitored by several INDOT operators. This project is to develop an automated and intelligent traffic condition monitoring system that will (1) automatically detect the traffic density, flow rate on each lane at all locations observed by the cameras, (2) identify the number and type of vehicles passing through each road, (3) detect start and end locations of traffic jams, (4) detect accidents, (5) prioritize the importance of different incidents and notify the traffic monitoring operators for all traffic incidents and (6) provide tools to the traffic monitoring operators to quickly gather the information of the incident scene. Future extension of this project will be to detect hazardous road conditions, such as black ice, snow accumulation by using the same system from this research.
Introduction
INDOT has installed many cameras and radars on Indiana’s highways to monitor traffic conditions
Proposed Architecture
Current Progress
Remaining Work in Future
Detect starting and ending locations of congestions and incidents
Improve the accuracy of the system
Develop algorithms for unlit roads (Current results only work in normal conditions)
Determine effective ways to clear a traffic jam
Develop methods to predict a traffic jam to prevent it from happening
Responses a traffic accident efficiently.
Improvement
Improve accuracy of vehicle detection algorithm by using tracking techniques
improve the accuracy of road and lane detection by using known and history information
Web Page Development
Detection Software Structure
Each camera is connected to a Desktop Computer. Each computer runs a python program for video processing and upload vehicle flow rate and speed in each lane to the database.
A
B
Field Camera
Field Computer
Field Computer
Field Computer
Field Camera
Field Camera
Office PC
Office PC
Office PC
C
The webserver and the database will work when they are on the same network as the cameras are.
The webserver connects to the database to retrieve required data and display it on website that can be accessed from the INDOT network.
First 1000 frame to get Road
Get Region of interest
Real-time Upload to Database
Detect vehicle flowrate of each lane
Get lane center positions and motion directions
Start of Traffic Congestions
Road Detection
Lane Detection
Traffic Flow Calculation
Incidents Detection
Traffic Jams
Using AI model (Yolo_v3+Tracking) for Vehicle Detection
Detect vehicle speed on each lane
Detect the motion of all observed vehicles
Calculate changes of vehicle flowrate, speed, and density
Detect vehicle density on each lane
Detect vehicles
End of Traffic Congestions
System diagnostics
AI model
Using AI model (Yolo_v3+Tracking) for Vehicle Detection
Lane and Vehicle Detection
Issues to be addressed:
Is there water accumulation on the road?
What is the snow accumulation level on the road?
Is there black ice on the road?
Are there debris on the road?
Currently, all these cameras are observed by human operators
Answers to these questions can help INDOT’s road maintenance team, the emergency response team, and driving condition notification team to perform more accurately and efficiently with real-time information. TASI proposes to answer these questions use the following information:
  Camera video streaming
  weather forecast information
  current weather information
  road snow plow/deicing history
and Artificial Intelligence algorithms to solve:
  Traffic flow rate and speed on each road and lane
  Starting point of the traffic jam
  Location of incidents
  Causes of the traffic jam
The work may also include the control of cameras in a scheduled motion pattern or automatic smart search patterns